## Slide 1
Revision 01
for project: 2024-184 part name: Unterteil
part number:CA00210 KTK mould number:WZ-1253
Customer mould number:61033006

## Slide 2
General Maintenance instructions
1.Before starting production生产前
Concerned area关注区域 | Action 动作 | When 开始时间
Molding forms 模具状态 Air vents排气 Parting line分型线 | Clean all lubrificant清洗所有的润滑油 Clean with a soft tissue or paper用很软的布或者纸巾清洗 | Before start 生产前
Concerned area关注区域 | Action 动作 | When 开始时间
Clamping force 锁模力 Tool safety模具安全性 Ejection pressure顶出压力 Hydraulic sliders pressure行位油缸的压力 Hot runner 热流道 | Verify the maintenance of the established values 根据已确认的数值来检查 | Every 1500 shots 每打1500啤时
Hydraulic circuit液压回路 Cooling circuit冷却回路 | Prevent leakage and established levels 确保防漏符合要求 Keep pipes and connectors in good conditions确保软管和接头连接正常 Keep the connection as per scheme 确保连接方式按照确定的方案执行 | 
Hot runner 热流道 Tool safety ：microswitch actuators and position elements 模具安全：限位开关和定位原件 | Prevent leakage防止泄漏 Keep the established levels保持已确认的标准 Verify condition of connectors ,cables and fixations 检查接线盒，线缆以及定位的状况 | Every 5000 shots 每打5000啤时
2.During production生产时

## Slide 3
3.After production生产后
Concerned area关注区域 | Action动作 | When开始时间
Molding forms 模具状态 Air vents排气 Parting line分型线 | Adjust if flash exists检查是否会有披锋存在 Check and correct pressure points检查并将压力调至正确值 Clean and oil清理油迹 | Every 30000shots for glass filled materials 加玻纤的材料每30000啤要检查一次 Every 60000 shots non-filled materials 没加填充剂的材料每60000啤要检查一次
Core cams导柱 Sliding bars 导向块 | Check the tightness of the hydraulics检查油缸的紧密性 Check the tightness of the cooling检查运水的紧密性 Check bushings condition检查导套的状态 Clean and oil 清理并打油 | 
Hydraulic ejection液压顶出Ejection plate顶针板 Ejectors顶针 Return pins回针 | Check the tightness of the hydraulics检查油缸的紧密性 Check the tightness of the cooling检查运水的紧密性 Check bushings condition检查导套的状态 Clean usage 确保装置回位 Clean and oil清理油迹 | 
Centering cone 直身锁 Pressure plate 压力板 | Check fitting area 检查封胶位区域 | 
Cooling circuit 冷却回路 Hydraulic circuit 液压回路 | Keep pre-establish tightness and flow rate 确保之前预置的密封性和流动性 Keep pipes and connectors good conditions确保软管和接头连接正常 Keep connection order 确保连接顺序正常 Replace the o-rings 更换密封圈 | 
Injection system浇注系统 | Check the tightness 检查密封性 Check usage of connectors, thermocouples And heating elements 检查连接头的使用，热电偶和加热器件的使用状况 Check usage of fixing and cables 检查定位和线缆的使用状况 | 

## Slide 4
4.Storage requirements存储要求
-When tool is not in production it should be drained of water 模具不生产的时候需要吹干所有水
-Form surfaces sprayed with protective layer to prevent corrosion 模具表面需要喷防锈油，防止生锈
-Place in an area where it cannot be damage 模具放在一个不会被碰坏的区域