## Slide 1
KTK mould Nr. | WZ-1276
Customer mould Nr. | 2025-154
Valid CAD file | 13077-655
Part name | CARRIER_NB5_MIKO
Part number | 13077-655
Material | >PP+TD20<
Color | white
Shrinkage flow direction | 1.013， pls confirm
Shrinkage cross direction | 1.013， pls confirm
Surface cavity | 4

## Slide 2
2. Parting Line / main demolding direction
3. Gate Locates
4. Ejection
8. Finish Require
1. Assembly situation
13. Proposals / part optimization
Content / mould
6. Mould body size / check with mould spec
12. Important measurements based on 2D
5. Sliders
9. Draft angle
10. Wall thickness
11. Engraving
7. Additional mould proposal
Content / part

## Slide 3
1. Assembly situation

## Slide 4
2. Parting lines / main demolding direction
Cavity
Core

## Slide 5
2. Parting lines / main demolding direction
红色线是前后模分型线
Pls confirm the main PL

## Slide 6
2. Parting lines / main demolding direction
绿色线是后模镶件夹口线
Pls confirm the PL of core insert

## Slide 7
3.1 Gate locations
尖点进胶
Mold Masters each part with 2 hot tip direct on part
Φ 3X0.5mm
Cut Φ3*0.5 on cavity side and add material on core side acc. , pls confirm
Φ 3X0.5mm

## Slide 8
4. Ejection
具体以3D为准
Ejector pin 顶针
斜顶 lifters
Blade Ejector Pin 扁顶针

## Slide 9
4. Ejection
紫色线为斜顶，直顶夹线，请确认
Pls confirm the PL of lifter

## Slide 10
5. Sliders
具体以3D为准
蓝色线为行位夹线
Pls confirm the PL of slider

## Slide 11
5. Sliders
蓝色线为行位夹线
Pls confirm the PL of slider
具体以3D为准

## Slide 12
5. Sliders
蓝色线为行位夹线
Pls confirm the PL of slider
具体以3D为准

## Slide 13
5. Sliders
蓝色线为行位夹线
Pls confirm the PL of slider
具体以3D为准

## Slide 14
6. Mould body size check with mould spec
GB
GB
GB
GB
GB
GB
GB
GB
码模板尺寸600m
码模板尺寸700mm
TOP
DATUM
超出注塑机大小，请更换注塑机
定位环：请提供
SR:请提供
ARBURG 470 C 1500-350 seems not suitable for this mold, waiting for your feedback

## Slide 15
8. Finish requirements

## Slide 16
9. Draft angle
Core：后模
Cavity ：前模
绿色面没有出摸角度，增加出摸角度
Can you add draft angel on green area?

## Slide 17
10. Wall thickness
箭头指示深红色区域成型后会有缩水印，
为防止产品表面有缩水风险，建议调整肉厚。
Red area with sink mark risk, is it OK?

## Slide 18
11. Engraving
1>PP+TD20<
Pls confirm engraving info. And location

## Slide 19
12. Important measurement based on 2D

## Slide 20
13. Proposals / part optimization
红色面位置倒扣，请修改产品
Red area with undercut, can you improve the part 3D?

## Slide 21
13. Proposals / part optimization
红色面位置倒扣，请修改产品
Red area with undercut, can you improve the part 3D?

## Slide 22
13. Proposals / part optimization
红色面位置倒扣，请修改产品
Red area with undercut, can you improve the part 3D?

## Slide 23
13. Proposals / part optimization
绿色面位置行位方向倒扣，请修改产品
green area with undercut on slider movement, can you improve the part 3D?
行位利角建议取消R角
Can we cancel this small R
On slider PL ?

## Slide 24
13. Proposals / part optimization
行位利角建议取消R角
Can we cancel this small R
On slider PL ?
绿色面位置行位方向倒扣，请修改产品
green area with undercut on slider movement, can you improve the part 3D?

## Slide 25
13. Proposals / part optimization
模肉
模胚
此温度感应器HY找不到资料和购买方，请是否可以如上图一样在模具中加上图中的孔即可，请确认，多谢！
This temp. sensor not available to buy it here, can we just make a hole in the mold acc. To above dimension?