## Slide 1
KTK mould Nr. | WZ-1278
Customer mould Nr. | /
Valid CAD file | 1-11286-11XX_C010286-03__G66_96_SPRITZLING_LI_BLENDE_C-SAEULE.stp
Part name | C_SÄULE LI
Part number | /
Material | >PC+ABS< T85X R50 black
Color | no
Shrinkage flow direction | 0,6%
Shrinkage cross direction | 0,6%
Surface cavity | /
Cavities : 1
update16,17,18

## Slide 2
2. Parting Line / main demolding direction
3. Gate Locates
4. Ejection
8. Finish Require
1. Assembly situation
13. Proposals / part optimization
Content / mould
6. Mould body size / check with mould spec
12. Important measurements based on 2D
5. Sliders
9. Draft angle
10. Wall thickness
11. Engraving
7. Additional mould proposal
Content / part

## Slide 3
1. Assembly situation

## Slide 4
2. Parting lines / main demolding direction
cavity
core
PL

## Slide 5
3. Gate locations
1个热流道尖点进胶
进胶位置，减胶φ5x0.5(深度)mm

## Slide 6
4. Ejection
Ø5 Ejector Pin 1pcs
Ø3 Ejector Pin 2pcs
Ø8 Ejector Pin 12pcs
Ø6 Ejector Pin 1pcs
活动顶块

## Slide 7
5. Sliders

## Slide 8
6. Mould body size check with mould spec
TOP
 |  | Current layout | o.k. / n. o. k.
tie bar horizontal | 450 |  | 
tie bar vertikal | 600 |  | 
mold hight min | 416 |  | 
mold hight max |  |  | 
centering ring cavity | Ø 120 |  | 
centering ring core | Ø 120 |  | 
nuzzle radius | 40 |  | 
模具尺寸：450x600x416mm

## Slide 9
7. Additional mould proposal

## Slide 10
8. Finish requirements
Cavity side:待客户提供
Core side:待客户提供

## Slide 11
9. Draft angle

## Slide 12
6. Proposal

## Slide 13
8. Important measurement based on 2D

## Slide 14
11. Wall thickness

## Slide 15
12. Engraving

## Slide 16
13. Proposals / part optimization
按客户2025-12-05图档，更新3D图档
Update the 3D drawing according to the client's drawing file 2025-12-05.

## Slide 17
13. Proposals / part optimization
按客户2025-12-05图档，更新3D图档
Update the 3D drawing according to the client's drawing file 2025-12-05.

## Slide 18
13. Proposals / part optimization
产品这里的R角，使行位分型面复杂，建议取消
取消R角后
After canceling the R-angle
The R-angle here in the product makes the slide position parting surface complex. It is recommended to cancel it.